## Slide 1
Presented by:
Noureldin Mostafa Galal
Mona Abdelrhman Mostafa
Farah Aksam Ibrahim
Toka Ramadan Mohamed
Mina Sameh Ibrahim
Mostafa Mortada Mohamed

## Slide 3
OUR PROJECT’S
  Analyze manufacturing downtime and machine failures.
  Support predictive maintenance and reduce production interruptions.
  Build a machine learning model for failure prediction.
  Evaluate machine and assembly line performance.
  Detect early warning signs of equipment failure.
  Identify critical failure indicators.
OBJECTIVES

## Slide 4
EQUIPMENT IDENTIFICATION
Every data point is anchored to a specific machine, location, and time.
MACHINE_ID
Assembly_Line_No
DATE
Makino-L1-Unit1-2013
Makino-L2-Unit2-2014
Makino-L3-Unit3-2015
DD/MM/YY
Shopfloor-L1
Shopfloor-L2
Shopfloor-L3

## Slide 5
PRESSURE SYSTEMS
FLUID POWER
The circulatory system of every CNC unit.
Hydraulic Pressure
COOLANT PRESUURE
Drives primary moving components measured in bar.
Ensure consistent flow at the tool workpiece interface.
Air System Pressure
Powers tool changes and debris clearing.

## Slide 6
MONITORING
THERMAL
  Heat is the enemy of precision.
  Thermal drift causes dimensional errors.
VIBRATION
DISPLACEMENT TRACKING
Spindle Bearing Temp (°C)
Prevents thermal expansion & accuracy loss.
Coolant Temperature.
Fluid thermal state at cutting zone.
Hydraulic Oil Temp(°C)
Viscosity & lubrication integrity.
Mechanical oscillations compromise surface finish and tool life. Measured in micrometers (µm).
Oscillation of the cutting tool itself.
Oscillation of the machine spindle assembly.
Tool Vibration
Spindle Vibration

## Slide 7
ELECTROCHEMICAL
KINEMATICS &
VOLTAGE (V)
Electrical Power Supply
SPINDLE SPEED (RPM)
Rational Frequency
TORQUE (Nm)
Reactive Mechanical Force
CUTTING FORCE (kN)
Materiak Resistance

## Slide 8
THE TARGET VARIABLE
OPERATIONAL STATUS
All sensor data converges on one critical classification
Operational
Machine Failure
Machine running within nominal tolerances no intervention needed
Critical fault or wear threshold reached triggers maintenance protocol

## Slide 9
DATA PREPROCESSING

## Slide 10
DUPLICATE RECORDS CHECK
Checked dataset for duplicate rows
Result: 0 duplicates found
DATE COLUMN CONVERSION
  Date column was originally stored in object/string format
  Converted Date column to proper datetime format
  Handled mixed date formats present in the data
  Ensured day-first format interpretation for correct date parsing

## Slide 11
MISSING VALUES IDENTIFICATIONS
HYDRAULIC PRESSURE (BAR) = 10
COOLANT PRESSURE (BAR) = 19
AIR SYSTEM PRESSURE (BAR) = 17
COOLANT TEMPERATURE = 12
VOLTAGE (VOLTS) = 6
TORQUE (NM) = 21
MISSING VALUES PRESENT ONLY IN NUMERIC/SENSOR COLUMNS. AFFECTED COLUMNS:
SPINDLE VIBRATION (ΜM) = 11
TOOL VIBRATION (ΜM) = 11
SPINDLE SPEED (RPM) = 6
HYDRAULIC OIL TEMPERATURE (°C) = 16
SPINDLE BEARING TEMPERATURE (°C) = 7
CUTTING (KN) = 7

## Slide 12
STRATEGIC IMPUTATION METHODOLGY
  Group-wise median imputation was applied to numeric columns, with the median calculated based on the simultaneous grouping factors of Machine_ID and Downtime status.
  Each missing value filled with the median of its corresponding group
  Preserves variation across machines and downtime status

## Slide 13
DATA VISUALIZATION

## Slide 14
FEATURE ENGINEERING

## Slide 15
FEATURE
ENGINEERING
Preparing raw manufacturing data for machine learning models.
Removed Date column as it was no longer required for modeling
Encoded target variable (Downtime) into binary format:
  Machine Failure → 1
  No Machine Failure → 0
Applied One-Hot Encoding on categorical features:
  Machine_ID
  Assembly_Line_No
Date Column

## Slide 16
TRAIN-TEST SPLIT.
• Separated dataset into Features (X) and Target (y).
• Split data into training and testing sets .
• Used 80% data for training and 20% for testing.
• Applied stratified splitting to maintain class balance between train and test sets.
• Fixed random state used for reproducibility of result.
→
→
→

## Slide 17
MACHINE LEARNING MODEL

## Slide 18
  Trained a random forest classifier on the training dataset.
  Used 200 decision trees (estimators) for building the model.
  Fixed random state used for reproducibility of results.
  Parallel processing enabled for faster training.
Accuracy → 98.80%
Precision→ 98.05%
Recall→ 99.60%
F1-Score → 98.82%
ROC-AUC→ 99.97%
Model shows excellent and well-balanced performance across all metrics
RANDOM FOREST MODEL

## Slide 19
FEATURE
IMPORTANCE ANALYSIS
Identified top features contributing to model's prediction using Random Forest's feature importance.
Top 4 features dominate the model's decision-making, together accounting for over 84% importance:
Torque (Nm)
⚙️
Hydraulic Pressure (bar)
🔧
Cutting Force (kN)
✂️
Coolant Pressure (bar)
💧
24.95%
21.60%
20.83%
16.74%
Spindle Speed (RPM) also shows moderate importance → 7.96%
Indicates that mechanical and pressure-related parameters are the strongest indicators of machine downtime

## Slide 20
  Trained an XGBoost Classifier on the training dataset
  Used 200 boosting rounds (estimators) Fixed random state used for reproducibility of results.
  Maximum tree depth set to 6
  Learning rate set to 0.1 for controlled and stable learning
  Log loss used as evaluation metric during training
  Fixed random state used for reproducibility of results
Accuracy→ 98.80%
Precision→ 98.05%
Recall → 99.60%
F1 Score → 98.82%
ROC-AUC Score → 99.98%
Model shows excellent and well-balanced performance across all metrics
XGBOOST MODEL

## Slide 21
FEATURE
IMPORTANCE ANALYSIS
Identified top features contributing to model’s prediction using XGBoost's feature importance
Hydraulic Pressure (bar)
🔧
44.32%
Dominant Predictor: Hydraulic_Pressure emerges as the primary leading indicator, accounting for 44.32% of the model's decision-making weight.
Secondary Mechanical Drivers: Torque and Cutting_Force follow in significance, contributing 21.40% and 15.16% respectively.

## Slide 22
CONCLUSION.

## Slide 23
THANK YOU